PRODUCT DESCRIPTION

OIL-UK SUPER XHS 5W-30 is a fully synthetic multigrade engine oil based on ultra-high quality synthetic base stocks and formulated with the very latest in advanced additive technology.

OIL-UK SUPER XHS 5W-30 has been developed to provide outstanding performance in the most up to date vehicles, which by their advancement in design have necessitated the employment of lighter viscosity multigrade engine oils while at the same time demanding more from the lubricant in terms of component protection, film strength and oxidation stability.

OIL-UK SUPER XHS 5W-30 responds to the demands of modern day motoring conditions by affording the highest level of performance and engine protection in the most severe conditions at both high and low ambient temperatures.

APPLICATIONS

OIL-UK SUPER XHS 5W-30 can be used in many types of passenger cars (petrol or diesel) including high performance turbocharged vehicles. It should not be used in vehicles fitted with diesel particulate filters.

FEATURES AND BENEFITS

- Excellent high and low temperature performance

- Exceptional long term anti-wear characteristics

- Very high standard of engine cleanliness

- Long lasting dispersant performance and corrosion protection

- Excellent sludge control for stop-go city motoring as well as long distances

- High temperature protection against ring sticking

- Reduced oil consumption and lower emissions

PERFORMANCE LEVEL SPECIFICATIONS

API: SM/CF

ACEA: A3/B4

Volkswagen:  502.00/505.00

Mercedes Benz MB: 229.5

General Motors: LL-A-025, LL-B-025

BMW: Longlife-01, Longlife-98

TYPICAL PHYSICAL DATA

| PROPERTY | TYPICAL VALUE |
| --- | --- |
| Specific Gravity @15.6°C | 0.874 |
| Kinematic Viscosity @ 100°C | 11.3 cSt |
| Kinematic Viscosity @ 40°C | 67.0 cSt |
| Viscosity Index | 155 |
| CCS @ -30°C | 6100Cp |
| Flash Point COC | 235°C |
| TBN (mg KOH/g) | 10.1 |
| Sulphated Ash (% w/w) | 1.26 |