DESCRIPTION

OIL UK ANGLO-MAX SUPER LDF-3 10W-40 is an ultra-high performance heavy duty diesel engine oil that provides outstanding protection, even under the most arduous operating conditions.

ANGLO-MAX SUPER LDF-3 10W-40 utilises formulation synergies which combine synthetic base oil systems and modern multi-function additive technology to deliver maintenance saving long drain performance and fuel economy capability, plus outstanding protection against acid formation, soot induced wear, and piston and engine deposits.

APPLICATION

ANGLO-MAX SUPER LDF-3 10W-40 is suitable for a wide range of trucking and transportation applications in vehicles using modern low-emission engines including Scania, Mercedes Benz, MAN, Renault, Volvo, Mack, MTU, Cummins, Deutz and many Japanese engine types

ANGLO-MAX SUPER LDF-3 10W-40 is formulated to satisfy the long drain interval requirements of most European engine manufacturers. It also provides the low emission performance and protection demanded for Euro 1, Euro 2, Euro 3, Euro IV, Euro V and Euro VI engines.

ANGLO-MAX SUPER LDF-3 10W-40 is also particularly suitable for Scania engines where piston cleanliness, oxidation, wear and emissions need to be finely controlled.  It should be used where a heavy duty diesel engine oil meeting the Scania LDF-3 specification is called for. ANGLO-MAX SUPER LDF-3 10W-40 is suitable for vehicles equipped with Exhaust Gas Recirculation (EGR) systems, and Scania vehicles fitted with Diesel Particulate Filters (DPF).

PERFORMANCE SPECIFICATIONS

- ACEA E4, E7

- API CF

- MTU  Type 3

- Mercedes Benz 228.5

- MAN M3277 (Up to 120,000km oil change intervals)

- Volvo VDS-3

- Scania LDF-3 (up to 90,000km oil change intervals)

- Deutz DQC III-05

- ZF TE-ML-04C

- DAF Extended Drain

- Renault Trucks RXD, RLD &  RLD-2, RLD-2, RD-2

- Mack EO-N

- EO-M Plus

- Cummins CES 20072

FEATURES AND BENEFITS

- Reduced Maintenance - Meets major engine manufacturer’s long oil drain requirements

- Fuel Economy – Reduced fuel consumption compared to higher viscosity grades

- Extended Engine Life – Exceptional wear protection

- Superior Engine Cleanliness – Superb piston cleanliness performance

- Enhanced environmental credentials

| TYPICAL PHYSICAL DATA |
| --- |
| Specific Gravity @ 15°C | 0.866 |
| Kinematic Viscosity @ 100°C (cSt) | 13.10 |
| Kinematic Viscosity @ 40°C (cSt) | 86.3 |
| Viscosity Index | 152 |
| Pour Point (°C) | -42 |
| Pour Point (°C) | 243 |
| Total Base Number mg KOH/g | 15.50 |