PRODUCT DESCRIPTION

OIL UK SUPER EURO FE 5W-30 is a state of the art, fully synthetic engine oil designed to offer the user exceptional fuel saving benefits. It achieves this by using a synergistic combination of premium synthetic base stocks, specialised polymers and performance additives blended to an optimised SAE 5W-30 viscosity grade.

Static engine tests and field trials have demonstrated that the chemistry employed by SUPER EURO FE 5W-30 is capable of delivering a typical fuel economy improvement of 2%, resulting in potentially huge savings on a fleet operator’s fuel bill. In addition, SUPER EURO FE 5W-30 is compatible with after-treatment devices fitted in modern heavy duty diesel engines such as diesel particulate filters and selective catalytic reduction units.

APPLICATIONS

OIL UK SUPER EURO FE 5W-30 is ideally suited for use in the very latest Euro 6 emission engines and is backwards compatible to older models. It is the perfect choice for a typical heavy duty fleet operator running a range of vehicle types and ages and who wishes to reduce fuel costs. SUPER EURO FE 5W-30 is not only well suited for use in trucks and buses but also in off-highway equipment such as large earth movers.

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD |
| --- | --- | --- | --- | --- |
| KMS: | 25,000 | 50,000 | 75,000 | 100,000 |

BENEFITS

- Exceptional fuel saving benefits

- Low volatility – reduced oil consumption

- Compatible with after treatment systems such as DPFs

- Outstanding soot handling properties

- Excellent low temperature pumpability

- Ideal for the latest Euro emission engines

- Outstanding anti-wear protection

PERFORMANCE LEVEL SPECIFICATIONS

ACEA E6, E9, E7,	API CJ-4/SN

MTU Category 3.1 Cummins CES 20081, Scania Low Ash, Voith Oil Class B, Caterpillar ECF-3

Mercedes Benz MB 228.51 MB 228.31, MB 235.28, MAN M3677, M3477, M3271-1,

Deutz DQC IV-10 LA, Volvo VDS-4 VDS-3, CNG, JASO DH-2, Detroit Diesel 93K218

Renault Trucks RXD, RLD-3 RLD-2, RGD, Mack EO-O PP, EO-N PP, EO-M PP

TYPICAL PHYSICAL DATA

| Test | Units | Test Method | Typical Properties |
| --- | --- | --- | --- |
| Specific Gravity @ 15.5°C | g/ml | ASTM D4052 | 0.855 |
| Kinematic Viscosity @ 100°C | cSt | ASTM D445 | 11.4 |
| Kinematic Viscosity @ 40°C | cSt | ASTM D445 | 69.7 |
| Viscosity Index |  | ASTM D2270 | 160 |
| Flash Point (Open) | °C | ASTM D92 | 226 |
| Pour Point | °C | ASTM D97 | -48 |
| Total Base Number | mg KOH/g | ASTM D2986 | 10.0 |
| Sulphated Ash | % wt |  | 0.99 |