DESCRIPTION

OIL UK SUPER EURO PLUS 10W-40 is a heavy duty diesel engine oil that has been formulated to meet the latest low SAPS criteria. It is based on fully synthetic base stocks combined with specialised performance additives to produce an engine oil which exhibits outstanding properties and long drain capabilities.

SUPER EURO PLUS 10W-40 meets ACEA E6, ACEA E9, ACEA E4 and ACEA E7, API CJ-4 as well as numerous OEM specifications, which gives it a very wide range of applications. SUPER EURO PLUS 10W-40 demonstrates enhanced characteristics in several key areas. These include improved soot handling, better resistance to oxidative thickening and increased protection against corrosion and wear.  SUPER EURO PLUS 10W-40 provides an impressive combination of reduced SAPS technology while still meeting some long drain full SAPS specifications.

All this means long predictable drain intervals with reduced down time and maintenance costs.

APPLICATIONS

OIL UK SUPER EURO PLUS 10W-40 is highly recommended for use in the majority of Euro IV, V and VI heavy duty diesel engines running under severe conditions and is also backwards compatible to older engines. It can be used in EGR engines, with or without diesel particulate filters, and in engines fitted with SCR NOx reduction systems. SUPER EURO PLUS 10W-40 is strongly recommended for engines fitted with diesel particulate filters and is designed for use in combination with low sulphur diesel fuel and can be used where any of the following specifications are required.

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD |
| --- | --- | --- | --- | --- |
| KMS: | 25,000 | 50,000 | 75,000 | 100,000 |

FEATURES AND BENEFITS

- Fully synthetic long drain formulation

- Low volatility – reduced oil consumption

- Compatible with after treatment systems such as DPFs

- Outstanding soot handling properties

- Excellent low temperature pumpability

- Ideal for the latest Euro emission engines

- Backwards compatible to older models

PERFORMANCE SPECIFICATIONS

ACEA E6, E9, E4, E7,	API CJ-4

MTU Category 3.1 Category 2.1, Cummins CES 20081, Scania Low Ash, Voith Oil Class B

Mercedes Benz MB 228.51 MB 228.31, MB 235.28, MAN M3477 M3575, M3271-1,

Deutz DQC IV-10 LA DQC III-10 LA, Volvo VDS-4 VDS-3, JASO DH-2, Renault Trucks RLD-3 RLD-2, Caterpillar ECF-3, Detroit Diesel 93K218, Mack EO-O Premium Plus EO-N Premium Plus,

OIL UK SUPER EURO PLUS 10W-40 can also be used in applications calling for New Holland specification MAT 3521.

TYPICAL PHYSICAL PROPERTIES

| Test | Units | Test Method | Typical Properties |
| --- | --- | --- | --- |
| Specific Gravity @ 15.5°C | g/ml | ASTM D4052 | 0.858 |
| Kinematic Viscosity @ 100°C | cSt | ASTM D445 | 14.3 |
| Kinematic Viscosity @ 40°C | cSt | ASTM D445 | 96.5 |
| Viscosity Index |  | ASTM D2270 | 153 |
| Flash Point (Open) | °C | ASTM D92 | 210 |
| Pour Point | °C | ASTM D97 | -34 |
| Total Base Number | mg KOH/g | ASTM D2986 | 12.6 |
| Sulphated Ash | % wt |  | 1.0 |