DESCRIPTION

Anglo-Max Super XDS-E5 10W-40 is a fully synthetic low SAPS engine oil for the latest Euro 5 and many Euro 6 commercial vehicle engines from manufacturers such as DAF, MAN and Mercedes Benz. Anglo-Max Super XDS- 5 10W-40 is an ultra -high performance diesel engine oil designed specifically to meet the challenge of the most severe lubrication requirements of the latest European and North American heavy duty diesel engines, particularly the low emission Euro 4, Euro 5 and Euro 6 engines running under the extreme demands of significantly extended oil change periods together with the clean performance requirements of these standards. Anglo-Max Super XDS-E5 10W-40 will provide the highest level of performance and protection in all HGV diesel engines where performance demands are severe and service periods are extended.

APPLICATION

Anglo-Max Super XDS-E5 10W-40 will provide the highest level of performance and protection in all Heavy Goods Vehicle diesel engines where performance demands are severe and service periods are extended.

FEATURES AND BENEFITS

- Suitable for Euro 4, Euro 5 and many Euro 6 engines

- Backwards compatible to older engines

- Exceptional long drain capabilities

- Low volatility providing reduced oil consumption and emissions

- Outstanding thermal stability offering consistent long term performance

- Effective environmental protection and fuel efficiency

- Outstanding anti-wear and anti-corrosion properties

- Excellent dispersant and acid neutralization characteristics

- Complete shear stability for extended stay in grade performance

PERFORMANCE SPECIFICATIONS

ACEA E6, E9, E7, API CI-4, MB 228.51, MAN M3477, M3271-1, RENAULT RVI RXD, RLD-2, RGD, MTU TYPE 3.1, VOLVO VDS-3, DAF EXTENDED DRAINS, CUMMINS 20076/77, MACK EO-N, EO-M PLUS, DEUTZ DQC IV-10 LA, DQC III-10 LA, DQC III-10

| TYPICAL PHYSICAL DATA | Unit | Test Method | Typical Data |
| --- | --- | --- | --- |
| Specific Gravity @ 15.5°C | g/ml | ASTM D4052 | 0.861 |
| Kinematic Viscosity @ 100°C | cSt | ASTM D445 | 14.2 |
| Kinematic Viscosity @ 40°C | cSt | ASTM D445 | 96.0 |
| Viscosity Index |  | ASTM D2270 | 152 |
| Flash Point (Open) | °C | ASTM D92 | 220 |
| Pour Point | °C | ASTM D97 | -35 |
| Total Base Number | mg KOH/g | ASTM D2986 | 10.1 |
| Sulphated Ash | % wt |  | 0.98 |