PRODUCT DESCRIPTION

OIL UK SUPER XHD 20W-50 is a Super High Performance heavy duty diesel engine oil formulated to meet the severe lubrication requirements demanded by many commercial vehicle manufacturers.

OIL UK SUPER XHD 20W-50 is a blend of solvent refined base oils and a highly sophisticated performance additive system to produce a heavy duty diesel engine oil that is suitable for a wide variety of major International trucks and buses used for inter-city or long haul applications.

OIL UK SUPER XHD 20W-50 offers extended oil drain periods and reduces unwanted sludge and varnishes in cylinders, valves and on pistons, even under highly stressed operating conditions.

APPLICATIONS

OIL UK SUPER XHD 20W-50 is suitable for both normally aspirated and turbocharged heavy duty diesel engines and is an ideal choice for use in a very wide range of heavy duty diesel engines such as those found in on-highway applications in trucks and buses as well as off-highway applications in the agricultural and construction sectors.

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD | VERY GOOD |
| --- | --- | --- | --- | --- | --- |
| KMS: | 7,500 | 15,000 | 20,000 | 30,000 | 40,000 |

- Greatly enhanced soot handling properties

- Contributes to effective oil filtration

- Improved protection of engine components

- Excellent engine cleanliness and oxidation control

- Reduced downtime due to unscheduled maintenance

- Long oil drain properties

PERFORMANCE LEVEL SPECIFICATIONS

API CH-4/ CF, SL/SJ

ACEA E3, A3/B3, A3/B4

Mercedes Benz 228.3, 229.1

MAN M3275

MTU Type 2

Mack EO-L

Volvo VDS-2

Renault RVI RD

TYPICAL PHYSICAL DATA

| Test | Units | Test Method | Typical Properties |
| --- | --- | --- | --- |
| Appearance |  | Visual | Clear and Bright |
| Specific Gravity @ 15.5°C |  |  | 0.892 |
| Kinematic Viscosity @ 100°C | cSt | ASTM D445 | 20.8 |
| Kinematic Viscosity @ 40°C | cSt | ASTM D445 | 188.9 |
| Viscosity Index |  | ASTM D2270 | 130 |
| Flash Point (Open) | °C | ASTM D92 | 220 |
| Pour Point | °C | ASTM D97 | -29 |
| Total Base Number | mg KOH/g | ASTM D2986 | 10.6 |