OIL UK ANGLO-MAX SUPER XHD HIGH VISCOSITY MONOGRADES SAE 60 & SAE 70 HEAVY DUTY DIESEL ENGINE OIL

DESCRIPTION

OIL UK ANGLO-MAX SUPER XHD 60 and XHD 70 are superior high viscosity classification non-multigrade engine oils, which are designed for use in very high ambient temperatures.

The combination of high viscosity solvent refined base oils and high technology additives is designed to give maximum protection to engines working for long periods under continuously arduous conditions in hot climates to provide comprehensive engine component protection.

The high performance additives systems used in these grades also prevent the build-up of carbon and lacquer deposits on piston ring grooves and valve stems, dramatically reducing the corrosive effects of the products of combustion.

APPLICATION

OIL UK ANGLO-MAX SUPER XHD 60 and XHD 70 may be used in a variety of turbocharged and naturally aspirated diesel engines operating in hot climates. Typical applications are earth movers, general plant equipment, large diesel generators and heavy goods vehicles.

FEATURES AND BENEFITS

- Excellent high temperature stability

- Improved bore polishing protection

- Excellent anti wear performance for reduced engine wear

- Excellent sludge control

PERFORMANCE SPECIFICATIONS

SAE 60: API CF-4

SAE 70: API CD