DESCRIPTION

Autotrans MVA is a next generation multi-vehicle automatic transmission fluid. One of the key features of Autotrans MVA is its anti-shudder performance in modern transmissions. Shudder can occur in transmissions using Slipping Torque Convertor Clutches which can lead to damage to the transmission. Autotrans MVA is designed to eliminate this problem.

Autotrans MVA is manufactured from ultra-high quality synthetic base oils, specially selected additives and friction modifiers to produce a lubricant with excellent oxidation stability and frictional characteristics.

APPLICATION

Autotrans MVA is recommended for the majority of modern automatic transmissions and power steering requirements in numerous automotive applications.

FEATURES AND BENEFITS

- Meets latest Voith specification

- Anti-shudder durability

- Wide range of applications

- Can be used as a power steering fluid

- Protection against wear

- Low foaming tendencies

- Extended drain capability

- High temperature stability

- Excellent low temperature properties

PERFORMANCE SPECIFICATIONS

| GM | Dexron IIIH | Ford | Mercon, Mercon V |
| --- | --- | --- | --- |
| JASO | 1A | Mercedes-Benz | MB 236.9 |
| Allison | C4, TES-295 | MAN | 339 Type V-1, Type Z-1, Z-2 |
| ZF | TE-ML 03D, 04D, 14A, 14B, 16L, 17C | Voith | H55.6335 |
| Volvo | 97340 & 97341 |  |  |

AUTOTRANS MVA is also suitable for use where the following are required:

| Manufacturer | Specification/Product |
| --- | --- |
| GM | Dexron IIIG, Dexron IIE, IID, II, Type A Suffix A, GM PN 22 689 186, GM PN 90 544 116 |
| Ford | Mercon V, Mercon, M2C-202B, M2C-919E, M2C-163A, M2C-166H, M2C-185A, M2C-922-A1, M2C-924A, R1-48 (BTR 4-Speed Auto), R1-28 |
| Allison | TES-228 |
| Caterpillar | TO-2 |
| Voith | SB013, SB118, G607 |
| ZF | TE-ML 09, 11A, 11B, 14C |
| MAN | 339A, 339D, 339F |
| Mercedes-Benz | MB 236.10 (Shell ATF 3403/M115), 236.11, 236.12 (ATF 3353), 236.3, 236.5, 236.6, 236.7, 236.8, 236.91, MB 001 989 2103 10 |
| VW Audi | G 055 025 A2, G 052 025 A2, G 052 162 A1 & A2 (Esso LT 71141, TL 52162), G 052 990 (09A), G 052 990 A2 (Texaco N402), G US 000 162 |
| Chrysler | ATF +4 (MS9602), ATF +3 (MS7176), ATF +2, ATF +, PN 04467721, AS68RC, SP-III |
| Honda | ATF-Z1 (except in CVTs) |
| Isuzu | Genuine, ATF II, ATF III |
| Nissan | Fluidmatic D, J, K & W, Nissan 402 |
| Saab | PN 93 165 147, Castrol Transmax J 3309, T-IV |
| Mitsubishi/Hyundai/Kia | SP, SP-II, SP-III, ATF Red-1K, Genuine ATF, ATF-J2 |
| Subaru | PN KO410Y0700, Castrol Transmatic J, Transmax J & E, Idemitsu H, ATF-HP |
| Toyota | Type T-IV (PN 08886-00405) (JWS 3309), T-III, T-II (PN 08886-80105), Type T |
| Volvo | PN 1161540, 1161640, 1161521, 1381167, Volvo Std 1273.41 |
| BMW | Shell LA2634, Shell M-1375.4, Texaco ETL 7045E, Texaco ETL 8072B, Esso LT 71141 |
| PSA Peugeot Citroën | PN PR 9980, Z 000 169 756 |
| Jaguar | Shell M-1375.4, Idemitsu K17 (JATCO) |
| Land Rover | Texaco N402, Shell M-1375.4 |
| Lexus | Type T, T-II (PN 08886-80105), T-III, T-IV (PN 08886-01705) |
| Mazda | ATF M-V, ATF M-III, F-1, JWS 3317, T-IV |
| Renault | Matic D2 |
| JASO | M315-2004 |
| Various | JWS 3314, JWS 3309 (Mobil ATF 3309), Idemitsu ATF HP, K17 |

| TYPICAL PHYSICAL DATA |
| --- |
| Kinematic Viscosity @ 40˚C (cSt) | 35.9 |
| Kinematic Viscosity @ 100˚C (cSt) | 7.5 |
| Viscosity Index | 183 |
| Density @ 20˚C | 0.843 |
| Pour Point (˚C) 0.844 | -52 |