OIL UK FLUSHING OIL

DESCRIPTION

All mineral oils are susceptible to oxidation even though the rate of oxidation is considerably retarded in those higher grade products (such as Oil-UK Therm Oils) based on specially refined oils and incorporating the correct anti-oxidants.

Mineral oil oxidation results in the formation of organic acids, alcohols, ketones and aldehydes most of which are soluble in the oil and increase its acidity and viscosity. In time, however, some of these compounds form insoluble gums, sludge and varnish on heater coils, causing reduced performance in heat transfer systems. Oil UK Flushing Oil removes such oxidation products and quickly restores cleanliness, thermal stability, efficiency and trouble trouble-free operation.

Oil UK Flushing Oil   is a blend of non-corrosive high flash point materials, completely soluble in mineral oil, which has a high solvent action on gums and varnishes. These oxidation products are loosened and held in suspension until the system is drained. Small amounts of water (less than 1%) in the oil system are dissolved.

APPLICATION

Best results are obtained by draining the system and then replacing with Flushing Oil. The system should then be operated for 100-150 hours before draining and filling with new oil.

Flushing Oil does not neutralise the acidic products of mineral oil oxidation. Therefore draining after the specified period is essential. After the use of Oil UK Flushing Oil all filters should be thoroughly cleaned before the introduction of new oil.

FEATURES AND BENEFITS

* High flash point compared with many solvent cleaners

* Exceptional solvent power for gums and varnishes

* Dissolves small amounts (less than 1%) of water

* Ease of application