OIL UK ANGLO-MAX SUPER XDS-E7 10W-40 HIGH PERFORMANCE SEMI-SYNTHETIC HEAVY DUTY DIESEL ENGINE OIL

DESCRIPTION

OIL UK ANGLO-MAX SUPER XDS-E7 10W-40 is an ultra-high performance semi-synthetic heavy duty diesel engine oil that provides outstanding protection, even under the most arduous operating conditions.

ANGLO-MAX SUPER XDS-E7 10W-40 utilises formulation synergies which combine synthetic and highly refined mineral base oil systems and modern multi-function additive technology to deliver maintenance saving long drain performance and fuel economy capability, plus outstanding protection against acid formation, soot induced wear, and piston and engine deposits.

APPLICATION

ANGLO-MAX SUPER XDS-E7 10W-40 is suitable for a wide range of trucking and transportation applications in vehicles using modern low-emission engines including Mercedes Benz, MAN,  Renault, Volvo, Mack, MTU, Deutz and many Japanese engine types

ANGLO-MAX SUPER XDS-E7 10W-40 is formulated to satisfy the long drain interval requirements of most European engine manufacturers. It also provides the low emission performance and protection demanded for Euro V engines.

PERFORMANCE SPECIFICATIONS

- ACEA E4, E7

- API CI-4

- MTU  Type 3

- Mercedes Benz 228.5

- MAN M3277

- Volvo VDS-3

- Renault Trucks RXD

- Mack EO-L

FEATURES AND BENEFITS

- Reduced Maintenance - Meets major engine manufacturer’s long oil drain requirements

- Fuel Economy – Reduced fuel consumption compared to higher viscosity grades

- Extended Engine Life – Exceptional wear protection

- Superior Engine Cleanliness – Superb piston cleanliness performance

- Enhanced environmental credentials

| TYPICAL PHYSICAL DATA |
| --- |
| Specific Gravity @ 15°C | 0.888 |
| Kinematic Viscosity @ 100°C (cSt) | 14.9 |
| Kinematic Viscosity @ 40°C (cSt) | 97.5 |
| Viscosity Index | 160 |
| Pour Point (°C) | -33 |
| Pour Point (°C) | 228 |
| TBN (mg KOH / g) | 14.12 |