DESCRIPTION

OIL UK ANGLO-MAX SUPER XDSS-E7 10W-40 is a semi-synthetic, fuel-efficient diesel engine oil meeting the latest long drain requirements of major engine manufacturers. This high performance heavy duty diesel engine oil has been specially formulated using highly refined pure mineral and synthetic base oils and state of the art technology performance additives.

The latest emission regulations have demanded more from diesel engine manufacturers, and Anglo-Max Super XDSS-E7 10W-40 has been designed to meet the exacting requirements of high performance, low emission engines up to and including Euro 5 units. This grade is also designed to be used over extended drain intervals.

APPLICATION

OIL UK ANGLO-MAX SUPER XDSS-E7 10W-40 is suitable for a wide range of normally aspirated and turbocharged heavy duty diesel engines in trucks, buses, coaches, plant and industrial equipment. It is miscible with all synthetic and mineral based engine oils.

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD | VERY GOOD |
| --- | --- | --- | --- | --- | --- |
| KMS: | 25,000 | 50,000 | 70,000 | 85,000 | 100,000 |

FEATURES AND BENEFITS

•	For use over extended drain intervals

•	High fuel efficiency and savings

•	Reduced oil consumption and emissions

•	Outstanding engine cleanliness and reduced engine deposits

•	Lower maintenance costs

•	Excellent high and low temperature stability

PERFORMANCE SPECIFICATIONS

API CI-4, ACEA E4, E7        MB 228.5 Mack EO-L MAN M 3277 Renault RXD MTU Type 3 Volvo VDS-3

| TYPICAL PHYSICAL DATA |
| --- |
| PROPERTY | UNIT | TEST METHOD | TYPICAL DATA |
| Specific Gravity @ 15.5°C | g/ml | ASTM D4052 | 0.888 |
| Kinematic Viscosity @ 100°C | cSt | ASTM D445 | 14.9 |
| Kinematic Viscosity @ 40°C | cSt | ASTM D445 | 97.5 |
| Viscosity Index |  | ASTM D2270 | 160 |
| Flash Point (Open) | °C | ASTM D92 | 228 |
| Pour Point | °C | ASTM D97 | -33 |
| Total Base Number | mg KOH/g | ASTM D2986 | 14.12 |