DESCRIPTION

OIL UK ANGLO-MAX SUPER XHS-FD 5W-30 is a high performance, fully synthetic motor oil formulated to provide improved fuel economy, excellent component protection and superior high temperature stability.

APPLICATIONS

OIL UK ANGLO-MAX SUPER XHS-FD 5W-30 is an ideal choice for normally aspirated and turbo-charged petrol and diesel engines where any of the following specifications are stipulated:

API: SL/CF, ACEA A5/B5, A1/B1

FORD: WSS-M2C913-D / WSS-M2C913-C, JAGUAR / LAND ROVER: STJLR.03.5003, RENAULT RN0700

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD |
| --- | --- | --- | --- | --- |
| KMS: | 10,000 | 20,000 | 30,000 | 40,000 |

FEATURES AND BENEFITS

- Extended oil drain capability

- Improved fuel efficiency

- Excellent high temperature stability

- Fully backwards compatible with earlier Ford Specifications: WSS-M2C913-A & 913-B

| TYPICAL PHYSICAL CHARACTERISTICS |
| --- |
| Kinematic Viscosity @ 100°C (cSt) | 9.53 |
| Kinematic Viscosity @ 40°C (cSt) | 51.50 |
| Viscosity Index | 172 |
| Flash Point (Closed) (°C) | 235 |
| TBN (mg KOH/g) | 10.20 |
| Pour Point (°C) | -38 |