DESCRIPTION

OIL UK HYLOAD HLPD 46 is a heavy duty detergent type ashless anti-wear hydraulic oil specially developed for machine-tool hydraulic systems, mobile hydraulic systems and clutch drives where minor water contamination can be expected. It is formulated with special detergents and dispersants to avoid valve blockage problems caused by contamination of oil with synthetic and/or semi-synthetic water based cutting fluids. HYLOAD HLPD 46 provides superior anti-wear properties, thermo-oxidative stability, rust &

corrosion protection, foam control and rapid air release properties and exceeds the performance requirements of HLPD classification of hydraulic oil and Daimler DBL 6721 specification.

The special detergent and dispersant properties of HYLOAD HLPD 46 ensure smooth functioning of hydraulic systems by minimizing formation of sticky residues and deposits. Excellent water emulsifying ability maintains proper functioning of hydraulic systems even in case of contamination of oil with small amounts of water. Superior anti-wear properties help reduce wear of mechanical components. High resistance to oxidation and thermal degradation controls the formation of sludge & varnish and improves oil life. Superior foam control and rapid air release properties ensure trouble-free operations and effective corrosion inhibitors provide corrosion protection in arduous service conditions.

APPLICATIONS

HYLOAD HLPD 46 is recommended for machine tool hydraulic systems where contamination of oil with water based cutting fluids is likely to occur and for mobile hydraulic systems and clutch drives where minor water contamination can be expected. Also for hydraulic systems in industrial and mobile service employing gear, vane and piston pumps where anti-wear hydraulic oils are recommended.

PERFORMANCE SPECIFICATIONS

DIN 51524/2 HLPD classification of hydraulic oils, Daimler DBL 6721

| TYPICAL PHYSICAL DATA |
| --- |
| PROPERTY | UNIT | TEST METHOD | TYPICAL DATA |
| Specific Gravity @ 15.5°C | g/ml | ASTM D4052 | 0.878 |
| ISO Viscosity Grade |  | ISO 3448 | 46 |
| Kinematic Viscosity @ 40°C | cSt | ASTM D445 | 46 |
| Viscosity Index |  | ASTM D2270 | 100 |
| Flash Point (Open) | °C | ASTM D92 | >185 |
| Pour Point | °C | ASTM D97 | <15 |
| Dispersancy strip test |  | DB.LA.4.042 | 65 |
| Steel Corrosion |  | DIN 51585 | O-B |
| Copper Corrosion |  | DIN 51759 - 100A3 | 1A |
| Timken OK Load |  | ASTM D2782 | 65 lb |
| Turbine Oil Stability Test |  | ASTM D943 | >3,500 hrs |
| FZG A/8.3/90: Load Stage Fail |  | DIN 51354-2 | >12 |