OIL UK MACHINE-LUB ZF High performance zinc-free circulation and hydraulic oil range

DESCRIPTION

OIL UK MACHINE-LUB ZF is a range of high quality zinc and ash free lubricants designed for hydraulic and circulation systems, where a premium quality zinc- free, ash- free fluid is desirable. The economical operation of a hydraulic and circulation systems system is dependent on the correct oil being used. Many modern machines use oils for the transmission of power from one component to another. The Oil UK Machine-Lub ZF range are manufactured from highly refined paraffinic base oils, which have good oxidation resistance lowering the possibility of gums and lacquers. They are blended using the latest in additive technology. The ash free additive pack used reduces the possibility of sludge and ensures rapid water separation.

APPLICATION

Oil UK Machine-Lub ZF grades are suitable for both hydrostatic and hydrodynamic circuits (with the exception of special automatic car transmissions), particularly when high aging resistance, antirust properties and demulsibility are required. Unlike many other hydraulic and circulating oils, these products contain anti-wear properties, and are therefore suitable for heavy duty applications where surface to surface lubrication protection is important. These oils are also suitable for use with air compressors.

FEATURES AND BENEFITS

- Compatible with all component metals, including silver

- Incorporates the latest corrosion inhibitors for protection against all forms of corrosion

- Highly shear stable

- Good anti foaming and air release properties

- High Viscosity Index

- Excellent demulsification characteristics for rapid water separation

- Improved filterability

- Good anti-wear performance for reduced wear in highly stressed vane pumps, highly loaded areas such as swash plates

High oxidation and thermal stability

OIL UK MACHINE-LUB ZF High performance zinc-free circulation and hydraulic oil range

PERFORMANCE SPECIFICATIONS

DIN 51524 Part 2 ISO 11158 ASTM D6158 SAE MS 1004 Eaton 35VQ25 AFNOR NFE 48603 (HM) Bosch Rexroth RE 90220 GM LS-2 (ISO 22 - 68) Sperry Vickers I-286-S Denison HF-0, HF-1 & HF-2 Cincinnati Milacron P-68 (ISO 32), P-70 (ISO 46), & P-69 (ISO 68)

TYPICAL PHYSICAL PROPERTIES

| VISCOSITY GRADE: | 32 | 46 | 68 | 100 | 150 |
| --- | --- | --- | --- | --- | --- |
| Specific Gravity @ 15.6°C | 0.873 | 0.878 | 0.880 | 0.889 | 0.890 |
| Kinematic Viscosity @ 40°C (cSt) | 32.0 | 46.0 | 68.0 | 100.0 | 150.0 |
| Kinematic Viscosity @ 100°C (cSt) | 5.36 | 6.75 | 8.75 | 2.62 | 3.38 |
| Viscosity Index | 101 | 101 | 102 | 101 | 99 |
| Flash Point °C | 215 | 220 | 224 | 231 | 239 |
| Pour Point °C | -33 | -32 | -31 | -27 | -25 |