OIL UK ANGLO-MAX SUPER XHD MONOGRADES SAE 10W, 20W, 30, 40 & 50 HEAVY DUTY DIESEL ENGINE OIL

DESCRIPTION

OIL UK ANGLO-MAX SUPER XHD MONOGRADES are superior quality single viscosity classification non-multigrade engine oils. The combination of solvent refined base oils and high technology additives is designed to give maximum protection to engines working under moderate to severe conditions, and also prevent the build-up of carbon and lacquer deposits on piston ring grooves and valve stems, dramatically reducing the corrosive effects of the products of combustion.

APPLICATION

OIL UK ANGLO-MAX SUPER XHD MONOGRADES may be used in a variety of turbocharged and naturally aspirated diesel engines where monograde viscosity lubricants are specified. Typical applications are earth movers, general plant equipment, large diesel generators, heavy goods vehicles, buses, vans and taxis. Anglo-Max Super XHD 10W and 30w are also suitable for use in many plant equipment hydraulic systems, transmissions and torque converters. Refer to manufacturer handbook.  Anglo-Max Super XHD Monogrades are miscible with all synthetic and mineral based engine oils

FEATURES AND BENEFITS

- Excellent high temperature stability

- Improved bore polishing protection

- Excellent anti wear performance for reduced engine wear

- Excellent sludge control

PERFORMANCE SPECIFICATIONS

API SL/CH-4/CF, MB 228.0 (All grades)

ACEA A3/B3, A3/B4, E2, MTU Type 1 (SAE 30, 40 & 50 only)

| TYPICAL PHYSICAL DATA |
| --- |
| PROPERTY | 10W | 20W | 30 | 40 | 50 |
| Specific Gravity @ 15.5°C | 0.880 | 0.882 | 0.885 | 0.891 | 0.895 |
| Kinematic Viscosity @ 100°C (cSt) | 5.50 | 8.21 | 10.78 | 15.20 | 20.51 |
| Kinematic Viscosity @ 40°C (cSt) | 33.41 | 62.02 | 91.02 | 142 | 223.02 |
| Viscosity Index | 100 | 100 | 102 | 109 | 107 |
| Flash Point (Open) (°C) | 212 | 214 | 218 | 235 | 240 |
| Pour Point (°C) | -30 | -30 | -30 | -30 | -30 |
| Total Base Number (mg KOH / g) | 10.26 | 10.21 | 10.29 | 10.24 | 10.21 |