PRODUCT DESCRIPTION

OIL UK ULTRAFARM SS 10W-40 is an advanced high performance universal oil designed for use in the latest agricultural machinery. It is also recommended in the majority of other off-highway equipment including construction, demolition and excavation.

OIL UK ULTRAFARM SS 10W-40 is prepared from a combination of synthetic hydrocracked and highly refined mineral base oils and is fortified with current state of the art additive systems. These provide the ultimate protection against wear and corrosion. This grade has superior shear stability and contains anti-foaming, anti-oxidation and demulsification additives, which are vital for satisfactory performance in engines, transmissions, final drives, hydraulic systems and wet brakes.

APPLICATIONS

OIL UK ULTRAFARM SS 10W-40 is suitable for use in naturally aspirated and turbocharged diesel and petrol engines, transmissions, hydraulic systems, final drives, wet brakes and oil immersed clutches.

PERFORMANCE LEVEL SPECIFICATIONS

SUPER UNIVERSAL TRACTOR OIL SPECIFICATIONS
 Massey Ferguson M1145, M1144,
 ZF TE-ML 03A TE-ML 06B, 06C,TE-ML 07B, 07D
UNIVERSAL TRACTOR TRANSMISSION FLUID SPECIFICATIONS
Massey Ferguson M1145, M1143, John Deere J20C, Ford M2C134-D
GEAR & TRANSMISSION SPECIFICATIONS
 API GL-4, Allison C4, Caterpillar TO-2, Afnor NFE 68603 E
ENGINE SPECIFICATIONS
 ACEA E3, API CG-4, CF-4, CF, CE/SF, MB 227.1, MAN 271, Ford M2C121-B CCMC D4,
US Military MIL-L-2104D

TYPICAL PHYSICAL DATA

Test	Units	Test Method	Typical Properties
Specific Gravity @ 15.5°C	g/ml	ASTM D4052	0.870
Kinematic Viscosity @ 100°C	cSt	ASTM D445	13.40
Kinematic Viscosity @ 40°C	cSt	ASTM D445	92.70
Viscosity Index		ASTM D2270	155
Flash Point (Open)	°C	ASTM D92	230
Pour Point	°C	ASTM D97	-38
Total Base Number	mg KOH/g	ASTM D2986	11.60