DESCRIPTION

Anglo-Max Super LSF 0W-30 is the latest new generation fully synthetic low SAPS (sulphated ash, phosphorus and sulphur) Multigrade engine oil formulated using ultra high quality base stocks and sophisticated additive chemistry.

APPLICATIONS

This product has been developed primarily for modern Ford vehicles requiring the WSS-M2C950-A specification. In addition, this product is recommended for applications requiring an ACEA C2, SAE 0W-30 specification making it suitable for a variety of models from manufacturers including Toyota, Honda and Kia.

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD |
| --- | --- | --- | --- | --- |
| KMS: | 10,000 | 20,000 | 30,000 | 40,000 |

FEATURES AND BENEFITS

- Exceptional low temperature properties

- Compatible with after treatment systems

- Long drain formulation

- Very high levels of engine cleanliness

- Fuel economy savings

- Unsurpassed levels of engine protection

- Excellent high and low temperature performance

- Tolerant of biodiesel contamination

PERFORMANCE SPECIFICATIONS

ACEA C2, FORD WSS-M2C950-A

| TYPICAL PHYSICAL CHARACTERISTICS |
| --- |
| Appearance | Clear & Bright |
| Specific Gravity @ 15.6˚C 0.848 | 0.841 |
| Kinematic Viscosity @ 100˚C (cSt) | 9.3 |
| Kinematic Viscosity @ 40˚C (cSt) | 43.1 |
| Viscosity Index | 203 |
| Flash Point (°C) | 216 |
| Pour Point (°C) | -50 |
| Sulphated Ash % Wt. | 0.79 |