DESCRIPTION

OIL-UK ANGLO-MAX SUPER XHS -F 5W-20 is a fully synthetic multigrade engine oil based on ultra-high quality synthetic base stocks and formulated with the very latest in advanced additive technology.

This highly ultra-high quality motor oil has been developed to provide outstanding performance in the most up to date vehicles, which by their advancement in design have necessitated the employment of lighter viscosity multigrade engine oils while at the same time demanding more from the lubricant in terms of component protection, film strength and oxidation stability.

OIL-UK ANGLO-MAX SUPER XHS -F 5W-20 provides significant fuel saving benefits as a result of its low viscosity and low friction technology, and has been specially formulated to meet the unique demands of Ford Motor Company Specification WSS-M2C948-B.

OIL-UK ANGLO-MAX SUPER XHS -F 5W-20 responds to the demands of modern day motoring conditions by affording the highest level of performance and engine protection in the most severe conditions at both high and low ambient temperatures. It also exhibits outstanding high and low temperature performance and excellent extra protection against corrosion and sludge formation.

APPLICATIONS

OIL-UK ANGLO-MAX SUPER XHS -F 5W-20 is particularly suitable for Ford 1.0L 3 Cylinder EcoBoost petrol engines, and for use in Ford 1.6l and 2.0L EcoBoost engines. It is also strongly recommended where an oil meeting Ford Specifications WSS-M2C948-B and WSS-M2C925-B are specified.

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD |
| --- | --- | --- | --- | --- |
| KMS: | 10,000 | 20,000 | 30,000 | 40,000 |

FEATURES AND BENEFITS

- Provides significant reductions in fuel consumption

- Superior oxidative stability

- Excellent low temperature fluidity

- High thermal stability

- Outstanding wear protection

- High level of shear stability

PERFORMANCE SPECIFICATIONS

API: SN/CF

ACEA: C5

Ford: WSS-M2C948-B / WSS-M2C925-B

ILSAC GF-5

Chrysler MS 6395

| TYPICAL PHYSICAL CHARACTERISTICS |
| --- |
| PROPERTY | TYPICAL VALUE |
| Kinematic Viscosity @ 100°C | 7.95 cSt |
| Kinematic Viscosity @ 40°C | 42.50 cSt |
| Viscosity Index | 161 |
| Flash Point COC | 200°C |
| Pour Point | -36°C |
| TBN (mg KOH/g) | 8.1 |
| Sulphated Ash (% w/w) | 0.78 |