DESCRIPTION

OIL UK ANGLO-MAX SUPER XHS 5W-40 is manufactured from fully synthetic base stocks and the latest additive technology available, providing a lubricant with outstanding performance and durability for the most demanding motorist. It offers quicker oil circulation for improved cold starting properties and higher lubricity for reduced internal friction compared with standard mineral based engine oils.

APPLICATIONS

OIL UK ANGLO-MAX SUPER XHS 5W-40 is suitable for normally aspirated and turbocharged petrol and diesel engines in passenger cars and light commercials and is suitable for all driving conditions. It is miscible with all synthetic and mineral based engine oils.

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD |
| --- | --- | --- | --- | --- |
| KMS: | 10,000 | 20,000 | 30,000 | 40,000 |

FEATURES AND BENEFITS

- Excellent high and low temperature stability

- Provides very high engine cleanliness

- Exceptional anti wear characteristics

- High temperature protection against ring sticking

- Reduced oil consumption and emissions

- Excellent sludge control

- Fuel efficient multigrade

PERFORMANCE SPECIFICATIONS

API SL/CF ACEA A3/B3, A3/B4, VW502.00, 505.00 MB 229.3, GM LL-B-025,

BMW Longlife-98, Renault RN0700, RN0710 Porsche A40

| TYPICAL PHYSICAL CHARACTERISTICS |
| --- |
| Specific Gravity @ 15.6°C | 0.849 |
| Kinematic Viscosity @ 100°C (cSt) | 14.7 |
| Kinematic Viscosity @ 40°C (cSt) | 93.0 |
| Viscosity Index | 165 |
| Flash Point COC (°C) | 223 |
| Pour Point (°C) | -36 |
| TBN (mg KOH / g) | 10.2 |