HIGH QUALITY LOW MINERAL OIL CONTENT SOLUBLE METALWORKING FLUID SPECIALLY DESIGNED FOR ARDUOUS CAST IRON MACHINING WITH MULTI-METAL POTENTIAL

PRODUCT DESCRIPTION

OIL-UK SOLCUT 3000 CF-I is a high quality, high lubricity, chlorine free semi synthetic cutting fluid specifically formulated to incorporate the latest advances in performance enhancing additive technology.

This product has been developed to provide high levels of boundary lubrication to give excellent machining performance without the use of environmentally unfriendly chlorine or sulphur EP additives.

Instead, superior synthetic lubricity additives have been incorporated to maximise machining performance and enhance surface finish. These combine in a highly bio stable micro-emulsion to provide extended sump life and improved tool life. OIL-UK SOLCUT 3000 CF-I provides the user with the very best in bio stability and corrosion protection performance demanded for cast iron machining, whilst also having the inherent flexibility to machine other materials.

APPLICATIONS

OIL-UK SOLCUT 3000 CF-I has been specially developed  for cast iron machining and to give cast iron engine block manufacturers greater machining flexibility and increased tool performance during difficult operations such as drilling and tapping where high levels of boundary lubrication is essential. The synthetic performance additives incorporated in the fluid provide outstanding surface finish on all types of ferrous metals and associated alloys in addition to arduous materials such as high tensile steels, titanium, copper and brass.

FEATURES AND BENEFITS

High resistance to bacteria attack

Low foam in high pressure systems

High Lubricity, providing superb hydrodynamic and boundary lubrication

Good machine tool cleanliness

Substantial corrosion protection Good machine tool cleanliness Odour-free Very economical in-use Excellent resistance to tramp oil contamination Superb surface finish

WATER COMPATIBILITY

- Typical 100 to 300 ppm (calcium carbonate) (soft to medium hard)

MATERIAL SUITABILITY AND RECOMMENDED CONCENTRATIONS

| Material Type | Performance Rating | Machining Applications | Recommended Concentration |
| --- | --- | --- | --- |
| Titanium | XXX | Broaching | 8-10% |
| Aluminium | XXX | Tapping | 6-10% |
| Aerospace Aluminium Alloys | XXX | Milling | 5-7% |
| High Alloy/Stainless Steels | XXX | Turning | 5-7% |
| Copper/Brass | XXX | Reaming | 8-10% |
| Cast Iron | XXXXX | Sawing | 5-8% |
|  |  | Drilling | 7-10% |

TYPICAL PHYSICAL DATA

| PROPERTY | TYPICAL RESULT |
| --- | --- |
| Appearance – Concentrate: | Amber fluid |
| Appearance - Emulsion | Translucent |
| Odour: | Bland |
| Specific Gravity – Concentrate: | 1.00 |
| Foaming Tendency (5% in 50 ppm water) | Low (Nil ml in 60 seconds) |
| Appearance - Emulsion | Clear Translucent |
| EP Performance | High |
| Reichert Lubricity Characteristics (10% dilution): Noise Reduction (Metres): Load Bearing Capacity (Kg/mm2): | 19.0 1.32 |
| IP287 Corrosion Test | 2.0% |
| IP125 Corrosion Test | 2.0% |
| Refractometer Factor | 1.9 |
| Ph @ 5% Emulsion | 9.2 |
| Aluminium Stain Test | No Stain |

Product Mixing:

OIL-UK advise the use of automated mixing systems. If mixing manually, always add the concentrate to the water with maximum agitation, if water is added to the concentrate, the emulsions may prove unstable. Avoid mixing with very cold concentrate or water. Check emulsion strength using a calibrated refractometer. Details of where to purchase equipment and how to use it are available from the OIL-UK Technical Department.

Product Management:

The working concentration should be carefully controlled and monitored on a daily basis as higher and lower working concentrations have health and safety implications. Machines should be cleaned out regularly. Fluid and particulate contaminants should be kept to a minimum. This is important especially in terms of bacterial control and is in line with the latest advice from government and professional sources. Detailed reference sources are quoted in the MSDS.

Storage:

- Store in a cool, well ventilated area

- Store inside, ideally between 10°C and 30°C

- Store away from direct heat and frost

- Shelf life 12 months from the date of manufacture

- Avoid water collecting on the barrel top