DESCRIPTION

OIL UK SUPER X-SN MOTOR OILS is a range of semi-synthetic engine oils designed to meet the lubrication requirements of modern petrol and diesel passenger cars and heavy duty commercial vehicles.

OIL UK SUPER X-SN MOTOR OILS meet the latest American Petroleum Industry (API) specifications and are suitable for use in all operating conditions, whatever the season.

APPLICATIONS

OIL UK SUPER X-SN MOTOR OILS are designed to give vehicle owners confidence of protection beyond that of conventional oils. They are particularly recommended for the following vehicle types and conditions:

- Stop / Go City Driving & Highway Cruising

- Latest engine technologies

- Gasoline and Diesel engine including naturally aspirated and turbo-charged and those that are fuel injected and multi-valved.

- Passenger cars, SUV’s, heavy duty commercial vehicles and light trucks and vans

- High performance engines

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD |
| --- | --- | --- | --- | --- |
| KMS: | 10,000 | 15,000 | 25,000 | 30,000 |

FEATURES AND BENEFITS

- Enhanced engine performance

- Long term wear protection of engine components, increasing engine life

- Outstanding soot handling properties

- Excellent low temperature pumpability

- Extended oil change intervals

- Excellent thermal and oxidation stability

PERFORMANCE SPECIFICATIONS

API: SN/CH-4,

ACEA: A3/B3, A3/B4, Mercedes: MB 229.1, Volkswagen VW 502.00, 505.00

| TYPICAL PHYSICAL CHARACTERISTICS |
| --- |
|  | Super X-SN Motor Oil Grade |
| Test | 10W-30 | 10W-40 | 15W-40 | 20W-50 |
| Specific Gravity @ 15.5°C | 0.860 | 0.866 | 0.868 | 0.886 |
| Kinematic Viscosity @ 100°C | 10 | 14.5 | 15.3 | 20 |
| Kinematic Viscosity @ 40°C | 64 | 95 | 114 | 180 |
| Viscosity Index | 141 | 153 | 140 | 129 |
| Flash Point (Open) | 220 | 225 | 226 | 235 |
| Pour Point | -33 | -33 | -35 | -36 |