DESCRIPTION

OIL UK ANGLO-MAX SUPER XHS 0W-20 is formulated to meet the extraordinary demands of high engine protection at a fuel-efficient low viscosity. It is produced using the highest quality synthetic base stocks together with state of the art additive chemistry. ANGLO-MAX SUPER XHS 0W-20 provides significant fuel saving benefits, exhibits outstanding thermal and oxidative stability and excellent protection against corrosion and black sludge.

APPLICATIONS

OIL UK ANGLO-MAX SUPER XHS 0W-20 is strongly recommended for many of the latest petrol engines in Honda, Toyota, Mazda and Suzuki vehicles. It can also be used where an SAE 0W-20 meeting the following API or ILSAC specifications is called for:

API SN, SN-RC

ILSAC GF-5

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD | VERY GOOD |
| --- | --- | --- | --- | --- | --- |
| KMS: | 10,000 | 15,000 | 25,000 | 35,000 | 40,000 |

FEATURES AND BENEFITS

- Provides significant reductions in fuel consumption

- Superior oxidative stability

- Excellent low temperature fluidity

- High thermal stability

- Outstanding wear protection

- High level of shear stability

PERFORMANCE LEVELS

API SN, SN-RC      ILSAC GF-5

TYPICAL PHYSICAL PROPERTIES

| OIL UK ANGLO-MAX SUPER XHS 0W-20 | Typical |
| --- | --- |
| Kinematic Viscosity @ 100˚C (cSt) | 8.1 |
| Kinematic Viscosity @ 40˚C (cSt) | 42.2 |
| Viscosity Index | 170 |
| Flash Point (COC,˚C) | 225 |
| Pour Point (˚C) | -43 |
| TBN (mg KOH/g) | 7.5 |
| Sulphated Ash (% wt) | 0.8 |