DESCRIPTION

OIL UK ANGLO-MAX SUPER LSH 0W-30 is a new generation fully synthetic multigrade engine oil formulated using the latest developments in synthetic technology together with the most up to date advancements in additive chemistry and sets new standards in engine oil performance.

ANGLO-MAX SUPER LSH 0W-30 has been developed to enable outstanding performance to be provided along with full compatibility with emission control after treatment systems. Low SAPS (sulphated ash, phosphorus and sulphur) additive technology allows optimum performance of these systems, including particulate filters, which ensures a high level of continuous pollution control thereby minimising environmental damage.

APPLICATIONS

ANGLO-MAX SUPER LSH 0W-30 is particularly suited to vehicles equipped with anti-pollution systems such as diesel particulate filters where the product’s low SAPS levels will greatly prolong the filter’s lifespan. These same features also ensure the maximum performance of catalytic converters since phosphorus and sulphur can impair the operation of such devices. This offers further environmental advantages by ensuring efficient treatment of exhaust gases.  Anglo-Max Super LSH 0W-30 is suitable for use in petrol and diesel engines.

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD |
| --- | --- | --- | --- | --- |
| KMS: | 10,000 | 20,000 | 30,000 | 40,000 |

FEATURES AND BENEFITS

- Compatible with Diesel Particulate Filters and Catalytic Converters

- Ensures lubricant performance over extended drain intervals

- Promotes fuel efficiency savings

- Very high standards of engine cleanliness

- Exceptional long term anti-wear and oxidation stability

- Excellent high and low temperature performance

PERFORMANCE SPECIFICATIONS

ACEA C2, API SN/CF

| TYPICAL PHYSICAL CHARACTERISTICS |
| --- |
| Specific Gravity @ 15.6°C | 0.846 |
| Kinematic Viscosity @ 100°C (cSt) | 9.70 |
| Kinematic Viscosity @ 40°C (cSt) | 52.50 |
| Viscosity Index | 173 |
| Flash Point (Closed) (°C) | 220 |
| Pour Point (°C) | -43 |
| TBN (mg KOH/g) | 7.2 |
| Sulphated Ash (% wt) | 0.78 |
| CCS @ -35°C (cP) | 5800 |