DESCRIPTION

OIL UK ANGLO-MAX SUPER FS 5W-30 is a fully synthetic, high performance, fuel economy engine oil meeting the requirements of the Ford WSS-M2C913-B specification. This high quality motor oil is a balanced blend of synthetic base stocks fortified with state-of-the-art additive technology which produces an exceptional engine oil offering enhanced protection and fuel economy.

APPLICATIONS

ANGLO-MAX SUPER FS 5W-30 is suitable for both normally aspirated and turbocharged petrol and diesel vehicles and is miscible with all semi synthetic and mineral oil based engine oils.

Typical oil change intervals (Always adhere to vehicle manufacturer’s recommendation)

| CONDITIONS: | SEVERE | DIFFICULT | MODERATE | GOOD |
| --- | --- | --- | --- | --- |
| KMS: | 10,000 | 20,000 | 30,000 | 40,000 |

FEATURES AND BENEFITS

- Extended drain capability • Excellent low temperature stability for improved flow rates • Provides fuel saving benefits • Fully synthetic formulation

PERFORMANCE SPECIFICATIONS

ACEA A5/B5, A1/B1 API SL/CF

Ford WSS-M2C913-B BMW Longlife-01 FE Opel Pass ILSAC GF-2

| TYPICAL PHYSICAL CHARACTERISTICS |
| --- |
| Specific Gravity @ 15.60°C | 0.857 |
| Kinematic Viscosity @ 100°C (cSt) | 10.80 |
| Kinematic Viscosity @ 40°C (cSt) | 62.50 |
| Viscosity Index | 165 |
| Flash Point (Closed) (°C) | 225 |
| Pour Point (°C) | -39 |
| TBN (mg KOH/g) | 8.9 |